## Slide 1: Blink the LED
By: Cread, Alex, Tony, Caleb

## Slide 2: Debugging: Steps to Resolving the “Illegal instruction” Error.

## Slide 3: “Illegal instruction” - Architecture
OLD: .cpu + .fpu
NEW: .arch armv6 + .fpu vfp
- PERIPH constants different for our version

## Slide 4: “Illegal instruction” - Outdated Instruction Set
- The real source of our Illegal instruction error.
- udiv is a relatively new instruction, not present in our older instruction set.
- Replaced udiv and voodoo math with a new modulus function:
--aebi-idivmod

## Slide 5: Final Bug
- Light would still not blink, everything seemed to be doing what it was supposed to do.
- Outdated instruction set = outdated documentation
-- Documentation for aebi-idivmod told us results were returned in certain
registers, but it was wrong!

## Slide 6
mov r3, PINS_IN_REG
mov r0, r5
mov r1, r3
bl __aeabi_idivmod
mov r2, r1
@ udiv r0, r5, r3
@ mul r1, r0, r3
@ sub r1, r5, r1
lsl r0, r0, 2
Red = Unsupported instruction causing
error, commented out
Green = Our instruction for udiv and
modulus, and for fixing registers.
Orange = Voodoo math, was
commented out
THE CODE

## Slide 7: Conclusion
- Architecture and other pre-processor concerns
- Outdated instruction set
- Wrong documentation